Click here to come back to the previous page
MAIN INPUT DATA FILE : 2D HEAT-DRIVEN CAVITY FLOW DIMENSIONLESS FORM : Ra= 1.D+06 Density scale : rho_0 (fluid density) Length scale H : height of cavity Velocity scale ---> U0= (k/H).Ra**0.25 (k thermal diffusivity) Temperature scale Th - Tc (Th= T hot ; Tc= T cold) Dimensionless Velocity U*= U/U0 Dimensionless Temperature T*= (T-Tc)/(Th-Tc) dimensionless kinematic viscosity= Pr/Ra**0.5 dimensionless thermal diffusivity= 1/Ra**0.5 dimensionless buoyancy term = Pr.T* dimensionless domain Lx/H= 1 , Ly/H= 1 Q0= 0 (adiabatic) --------------------------------- | | | | | | | | | | Th | | Tc | | | | | | | | | | | | --------------------------------- Q0= 0 (adiabatic) J | | | ----> I =========================================================================== =========================================================================== ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ GENERAL LAYOUT ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ &Version File_Version="VERSION2.0"/ =========================================================================== FLUID PROPERTIES (DIMENSIONLESS FORM) =========================================================================== &Fluid_Properties Heat_Transfer_Flow = .true. , Reference_Density= 1.0, Reference_Temperature= 1.0 , Reference_Dynamic_Viscosity= 0.71D-03 , Prandtl = 0.71 , Thermal_Expansion_Coefficient= 1.0 / =========================================================================== UNIFORM INITIALIZATION OF THE VELOCITY COMPONENTS AND TEMPERATURE (DIMENSIONLESS FORM) =========================================================================== &Velocity_Initialization I_Velocity_Reference_Value = 0.0 , J_Velocity_Reference_Value = 0.0 , K_Velocity_Reference_Value = 0.0 / &Temperature_Initialization Temperature_Reference_Value = 0.5 / =========================================================================== GRAVITY (DIMENSIONLESS FORM) =========================================================================== &Gravity Gravity_Enabled= .true. , Gravity_Angle_IJ= 90.0 , Gravity_Angle_IK= 90.0 , Reference_Gravity_Constant= 0.71/ =========================================================================== DOMAIN FEATURES =========================================================================== &Domain_Features Start_Coordinate_I_Direction= 0.00 , End_Coordinate_I_Direction= 1.00, Start_Coordinate_J_Direction= 0.00 , End_Coordinate_J_Direction= 1.00, Start_Coordinate_K_Direction= 0.00 , End_Coordinate_K_Direction= 0.00, Cells_Number_I_Direction= 256 ,Cells_Number_J_Direction=256 ,Cells_Number_K_Direction= 1, Regular_Mesh= .true. / ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ DEFINITION OF BOUNDARY CONDITIONS ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ ============================================================================= WALL BOUNDARY CONDITION SETUP ============================================================================= &Heat_Wall_Boundary_Condition_Setup West_Heat_BC_Option = 0 , East_Heat_BC_Option = 0 , Back_Heat_BC_Option = 1 , Front_Heat_BC_Option = 1 , South_Heat_BC_Option = 0 , North_Heat_BC_Option = 0, West_Wall_BC_Value= 1.0 , East_Wall_BC_Value= 0.0 , Back_Wall_BC_Value= 0.0 , Front_Wall_BC_Value= 0.0 , South_Wall_BC_Value= 0.0 , North_Wall_BC_Value= 0.0 , End_of_Data_Block= .true. / ============================================================================= BORDER BOUNDARY CONDITIONS : The walls located by default at the ends of the domain remain unchanged ============================================================================= &Border_Domain_Boundary_Conditions West_Border= 0 , East_Border= 0 , Back_Border= 0 , Front_Border= 0 , North_Border = 0 , South_Border = 0 / ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ NUMERICAL METHODS ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ Navier-Stokes equations ---> BDF2 + 2nd order centered scheme , semi-implicit convection flux ---> conservative form Poisson ---> Relaxed Gauss-Seidel method + Multigrid &Numerical_Methods Numerical_Scheme= 1 , Convective_Flux_Discretization_Type = 1 , Temperature_Advective_Flux_Discretization_Type = 1 , Explicit_Solving_of_Density = 0 , Velocity_Correction_Enabled = .true., Numerical_Method_Poisson_Equation = 1 , Number_max_Grid= 5, Number_max_Cycle= 10 , Number_Iteration= 15 , Relaxation_Coefficient= 1.7 , Convergence_Criterion= 1.D-10 / ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ SIMULATION MANAGEMENT ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++ The numerical time step is estimated by means of the CFL coefficient &Simulation_Management Restart_Parameter= 0 , Steady_Flow_Stopping_Criterion_Enabled = .true. , Steady_Flow_Stopping_Criterion = 1.D-16, Temporal_Iterations_Number = 1000000 , Final_Time = 5.D+02 , TimeStep_Type = 0 , Timestep_Min = 1.D-03 , Timestep_Max = 1.D-03 , CFL_Min = 0.5 , CFL_Max = 0.5 , Iterations_For_Timestep_Linear_Progress= 1, Simulation_Backup_Rate = 1000 , Simulation_Checking_Rate = 101 / ============================================================================= PROBES MANAGEMENT ============================================================================= NO PROBE ============================================================================= FIELDS RECORDING DECLARATION ============================================================================= &Simulation_Management Fields_Recording_Rate = 5.D+01 / &Field_Recording_Setup Check_Special_Features= "Heat_Driven_Cavity_Flow", Precision_On_Instantaneous_Fields= 2 / Here, a special variable devoted to results of heat driven cavity flows is active &Instantaneous_Fields_Listing Name_of_Field = "U " , Recording_Enabled = .true. / First velocity component &Instantaneous_Fields_Listing Name_of_Field = "V " , Recording_Enabled = .true. / Second velocity component &Instantaneous_Fields_Listing Name_of_Field = "T " , Recording_Enabled = .true. , End_of_Data_Block= .true. / Temperature

Click here to come back to the previous page