## Namelist "Gravity"
This data set is related to the characteristics of the gravity force.
If no gravitational effect is considered, this namelist can be omitted.
## Full data set of the namelist
  &Gravity Gravity_Enabled= .true. ,
        Gravity_Angle_IJ= 0.0 ,
        Gravity_Angle_IK= 90.0 ,
        Reference_Gravity_Constant= 9.81D+00/

## Definition of the data set

### Gravity_Enabled
- Type : boolean value
- The gravity effects are enabled or disabled
- Default value= .false.
### Gravity_Angle_IJ
- Type : real value
- Angle between the I-axis and of the projection of on the IJ-plan (in degrees). The I-axis is the origin axis.
- Default value = 0.0
### Gravity_Angle_IK
- Type : real value
- angle between the K-axis and (in degrees). The K-axis is the origin axis.
- Default value = 0.0
### Reference_Gravity_Constant
- Type : real value
- Reference value of the gravity constant
- Default value = 9.81

## IMPORTANT NOTE

The orientation of the gravity vector in the cartesian referential is defined from the below formulation (spherical coordinates) : / Where is norm of the force of gravity (or the buoyancy force). Remarks / The angle ranges are Gravity_Angle_IJ and Gravity_Angle_IK . / From the definition of angles, note that the vector is oriented along the axis while Gravity_Angle_IK= 0 and is in the plan IJ while Gravity_Angle_IK= 90. / Following the type of simulation and the choice on the form of equations (dimensional, dimensionless, the scales used in order to define the non-dimensional form of equations, etc …), the term can be written following different ways. For instance, the buoyancy force can be read as : in the momentum equations under Low Mach number hypothesis. In this case / where is the constant of gravity. / is the reference density defined in the namelist "Fluid_Properties". / The buoyancy force can also be read as : in the momentum equations for incompressible flows under Boussinesq hypothesis. In this case / where is the thermal expansion coefficient of the fluid considered. / is the reference temperature defined in the namelist "Fluid_Properties". / As a consequence the generalized form of in the code is : where is defined from the data “Reference_Gravity_Constant” and from the data “Thermal_Expansion_Coefficient” (in the namelist "Fluid_Properties" ). The Default values of these variables are : / Reference_Gravity_Constant= 9.81 / Thermal_Expansion_Coefficient = 1.0 / These values are automatically taken into account by the code if these variables are not explicitly modified by the user in the data file. Clearly, the variable “Thermal_Expansion_Coefficient” is only needed in the simulations of incompressible flows with thermal buoyancy effect . In every other cases, it can be omitted because the buoyancy/gravity force can be defined from the variable “Reference_Gravity_Constant” only.