## Namelist "Temperature_Initialization"
This data setup is used to define the initial temperature field over the domain for flows with heat transfer.
This namelist can be removed for isotherm flows.
## Full data set of the namelist
&Temperature_Initialization Temperature_Reference_Value = 293.0,
        Initial_Field_Option_For_Temperature= 0 ,
        White_Noise_Magnitude_For_Temperature= 0.0 /
For low Mach-number flows, the user must ensure the coherence between the reference values of physical quantities defined in the namelist "Fluid_Properties" (temperature, density and molecular mass), the initial temperature field over the domain (defined here) and, if needed, the species mass fraction distribution defined in the namelist "Species_Initialization" (if the gas is composed with multi-components). Keep in mind that the reference value of thermodynamic pressure is calculated from the reference values of temperature, density and molecular mass of the fluid (see namelist "Fluid_Properties"). The density field is then initialized from the fields of temperature (and species mass fractions if needed) by considering the thermodynamic pressure is uniform over the domain (low Mach-number hypothesis).

## Definition of the data set

### Temperature_Reference_Value
- Type : real value
- Reference temperature value.
- Default value must be set by the user
### Initial_Field_Option_For_Temperature
- Type : integer value
- Option to define the distribution of the temperature over the domain :
  - 0 : Uniform distribution
  - 1 or greater : Optional values associated to temperature field defined by the users in the appropriate fortran module (see module_user_define_init_fields.f90). The reference value can be used to define the temperature scale.
  - Default value = 0
### White_Noise_Magnitude_For_Temperature
- Type : real value
- Magnitude of the white noise on the temperature field.
- The magnitude is defined as a fraction of the local value in each cell ( i.e. 0.4 corresponds to 40% of the local value of temperature on the grid)
- Default value = 0