### The physical properties for an incompressible fluid without multi-species components
We report here the dimensionless data set about the fluid properties defined above.
  &Fluid_Properties Variable_Density = .false. , !---- Incompressible fluid
        Constant_Mass_Flow = .true. , !---- The mass flowrate is constant
        Heat_Transfer_Flow = .true. , !---- Heat transfer enabled
        Reference_Density = 1.0 , !---- Dimensionless fluid density
        Reference_Dynamic_Viscosity = 1.D-02 , !---- Dimensionless dynamic viscosity (=1/Reh)
        Reference_Temperature = 1.0 , !---- Dimensionless reference temperature (=Tc*)
        Prandtl = 0.71 , !---- Prandtl number value
        Thermal_Expansion_Coefficient= 1.0 / !---- Dimensionless thermal expansion coeffficient
The heat capacity of the fluid is not set here because unuseful. For incompressible flows without multi-species components, the enthalpy equation is reduced to an advective-diffusive transport equation for temperature. Only the thermal must be defined which is directly computed from the “Reference_Dynamic_Viscosity”, the “Reference_Density” and the “Prandtl” values. For more examples about the fluid properties setting click here.

Go to the page Tutorial : How to build the input data file ?