### Output data
Here we show an example of usual data acquisition :
- Instantaneous fields
- Statistical fields
- Time series from probes located at specific positions
The various parameters related to each type of output data are originally splitted by topic in the appropriate namelist. For a sake of clarity, they are directly regrouped for each type of output data as shown here :
For instantaneous fields
&Field_Recording_Setup Precision_On_Instantaneous_Fields= 2 / !--- option value for writing results in double precision (1 = single precision)
&Simulation_Management
     InstantaneousFields_RecordingReset=.false. , !--- Reset to zero the file number ID
     InstantaneousFields_TimeRecordingRate= 5.0E-01 , !--- Recording rate in "time unit"
     InstantaneousFields_RecordingStartTime= 1.D-00 , !--- Threshold from which the recording begins (used with InstantaneousFields_TimeRecordingRate only)
  ! InstantaneousFields_TimeIterationRecordingRate= 10 , !--- Recording rate in "time-step iteration unit (number of time steps)"
  ! InstantaneousFields_StartTimeIterationRecording= 70 !--- Threshold from which the recording starts (used with InstantaneousFields_TimeIterationRecordingRate only)
     /
&Instantaneous_Fields_Listing Name_of_Field = "U" / !--- Recording of the first velocity component enabled
&Instantaneous_Fields_Listing Name_of_Field = "V" / !--- Recording of the second velocity component enabled
&Instantaneous_Fields_Listing Name_of_Field = "W" / !--- Recording of the Third velocity component disabled
&Instantaneous_Fields_Listing Name_of_Field = "T" / !--- Recording Temperature enabled
&Instantaneous_Fields_Listing Name_of_Field = "P" / !--- Recording Pressure enabled
For statistical fields
&Simulation_Management Start_Time_For_Statistics= 1.D+2 , !--- Start time for computing the statistical fields
        Time_Range_Statistic_Calculation = 1.D+00 / !--- time range over which the statistical field computation is performed.
        When it has been covered, the results are recorded and a new statistical computation starts again
&Field_Recording_Setup Precision_On_Statistical_Fields= 2 , !--- option value for writing results in double precision (1 = single precision)
        Time_Statistics_Enabled= .true. , !--- time statistics are performed (true) - classical statistics (false)
        Sample_Rate_For_Statistics= 1 , !--- Sample rate (in time iteration unit)
        Statistic_Space_Average_Type= "NO_SPACE_AVERAGE" / !--- option on spatial averaged fields
&Statistical_Fields_Listing Name_of_Field = "<U> " / !---- Averaged I-velocity component
&Statistical_Fields_Listing Name_of_Field = "<V> " / !---- Averaged J-velocity component
&Statistical_Fields_Listing Name_of_Field = "<P> " / !---- Averaged pressure
For time-series from probes
        U , V , W , T , P , RHO
&Probe_Quantities_Enabled Temporal_Series_For_Quantity_Enabled(:)= .true. , .true., .false., .false., .true., .false. / !--- Selection of physical quantities
&Simulation_Management
        Probe_TimeIterationRecordingRate= 2 , !--- Recording rate in "time-step iteration unit (number of time steps)"
        Probe_RecordingReset=.false. , !--- if True, Time series are written in new files (with the same name), previous data are removed
        Probe_StartTimeIterationRecording= 20 !--- Threshold from which the recording starts
       /
&Probe_Location Xi= 2.0 , Xj= 1.5 , Xk= 0.0 / !---coordinates of probe 1
&Probe_Location Xi= 3.0 , Xj= 1.0 , Xk= 0.0 / !---coordinates of probe 2
Any information about these namelist are available here : / Simulation_Management / Field_Recording_Setup / Instantaneous_Fields_Listing / Statistical_Fields_Listing / Probe_Quantities_Enabled / Probe_Location