===========================================================================
===========================================================================
         MAIN INPUT DATA FILE : 2D EDDY ON A PERIODIC DOMAIN (DIMENSIONAL RELEASE)

Initialization of the velocity field carried out from the user's routine Eddy_Velocity_Field in the module named module_user_define_init_fields.f90
                                     access --->  Initial_Field_Option_For_Velocity_I= 4 

===========================================================================
===========================================================================
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
                     GENERAL LAYOUT
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
&Version File_Version="VERSION2.0"/
===========================================================================
                FLUID PROPERTIES
===========================================================================

&Fluid_Properties  Reference_Density= 860.0 , Reference_Dynamic_Viscosity = 43.D-03 /

===========================================================================
   INITIALIZATION OF THE VELOCITY COMPONENTS, THE TEMPERATURE AND SPECIES
===========================================================================
Initial_Field_Option_For_Velocity_I : Special initialisation of a 2D eddy defined by the user's routine Eddy_Velocity_Field 
                                      in the module named module_user_define_init_fields.f90

&Velocity_Initialization I_Velocity_Reference_Value= 0.00 , J_Velocity_Reference_Value= 0.00, K_Velocity_Reference_Value= 0.00 , Initial_Field_Option_For_Velocity_I= 4 /
===========================================================================
                GRAVITY 
===========================================================================

No gravity 

===========================================================================
                    DOMAIN FEATURES
===========================================================================

&Domain_Features Geometric_Layout= 0,  
                 Start_Coordinate_I_Direction=-0.50 , End_Coordinate_I_Direction= 0.50, 
                 Start_Coordinate_J_Direction=-0.50 , End_Coordinate_J_Direction= 0.50, 
                 Start_Coordinate_K_Direction= 0.00 , End_Coordinate_K_Direction= 0.00, 
                 Cells_Number_I_Direction= 128  ,Cells_Number_J_Direction= 128 ,Cells_Number_K_Direction= 1,
                 Regular_Mesh= .true. /

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
              DEFINITION OF BOUNDARY CONDITIONS
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
=============================================================================
                 WALL BOUNDARY CONDITION SETUP 
=============================================================================
 No wall
=============================================================================
               INLET AND OUTLET BOUNDARY CONDITIONS
=============================================================================
No inlet, No outlet
=============================================================================
               BORDER BOUNDARY CONDITIONS
=============================================================================
&Border_Domain_Boundary_Conditions West_Border= 4 , East_Border= 4 , Back_Border= 4 , Front_Border= 4 , North_Border = 0 , South_Border = 0 /
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
                   NUMERICAL METHODS
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
 Default initialization:

 Numerical scheme for Navier-Stokes equations : 2nd centrered order in space, 2nd order in time (BDF2 : 2nd oder Backward Differentiation Formulation)
                  for Poisson equation        : SOR iterative method coupled with a multigrid approach

Parameters for solving Poisson equation (multigrid parameters) :

&Numerical_Methods  Numerical_Scheme= 1 ,
                    Convective_Flux_Discretization_Type = 1
                    Numerical_Method_Poisson_Equation= 1,
                    Number_max_Grid= 6 , Number_max_Cycle= 5 , Number_Iteration= 15 ,
                    Relaxation_Coefficient = 1.80 , Convergence_Criterion = 1.D-10 /

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
                   SIMULATION MANAGEMENT
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

Time step calculated from a CFL coefficient

&Simulation_Management    Restart_Parameter= 0 , 
                          Steady_Flow_Stopping_Criterion_Enabled = .true. , Steady_Flow_Stopping_Criterion = 1.D-22, 
                          Temporal_Iterations_Number = 50000                  , Final_Time = 2.0D+01  , 
                          TimeStep_Type = 1 ,
                          CFL_min= 0.25   , CFL_max= 0.25, Iterations_For_Timestep_Linear_Progress= 1 ,
                          Timestep_Min = 2.D-01                           , Timestep_Max = 2.D-01 , 
                          Simulation_Backup_Rate                 =  200   , Simulation_Checking_Rate = 51  /

=============================================================================
                   PROBES MANAGEMENT
=============================================================================
                                                      Probes order    U    , V     , W      , T      , P      , RHO
&Probe_Quantities_Enabled  Temporal_Series_For_Quantity_Enabled(:) = .true., .true., .false., .false., .true. , .false. / 

&Probe_Location  Xi= 0.0 , Xj= 0.0 , Xk= 0.0  /
&Probe_Location  Xi= 0.1 , Xj= 0.1 , Xk= 0.0 , End_of_Data_Block= .true. /
&Simulation_Management   Probe_Recording_Rate = 1 /


=============================================================================
           FIELDS RECORDING DECLARATION
=============================================================================
&Field_Recording_Setup  Precision_On_Instantaneous_Fields= 2 /
&Simulation_Management  Fields_Recording_Rate = 1.0D-00 /

&Instantaneous_Fields_Listing  Name_of_Field = "U" , Recording_Enabled = .true.  /      First velocity component
&Instantaneous_Fields_Listing  Name_of_Field = "V" , Recording_Enabled = .true.  /      Second velocity component
&Instantaneous_Fields_Listing  Name_of_Field = "W" , Recording_Enabled = .false. /      Third velocity component
&Instantaneous_Fields_Listing  Name_of_Field = "P" , Recording_Enabled = .true.  /      Pressure related to the velocity field